## Slide 1: Title slide + image
Gait Detection using Wrist-worn IMUs for Home
Rehabilitation of Stroke Patients
Hendrik Böckenhauer Tatiana Orlovskaia
Supervised by dr. Herwin Horemans & dr. Arkady Zgonnikov
Notes: Structure:
Intro + motivation
Relavant work
Methodology : signal processing + ML
Results
Discussion + conclusion
Today we will be talking about ….

## Slide 2: TU Delft
Create/edit a Hyperlink TO A SLIDE
1
Go to the tab ‘Insert’ and click on the button ‘Shapes’. Choose the shape ‘Rectangle’ and drag the mouse over the slide to create a shape.
2
Drag the shape over the menu button and scale the shape as large as the button. Click with the right mouse button on the shape and choose ‘Edit shape’.
3
Click on the paint bucket icon, click on ‘Shape Fill’ and drag the ‘Transparency’ slider to 100%. Now the shape is completely transparent.
Shapes
Size and position…
Edit shape…
Transparency
100%
4
Click on the transparent shape and use the shortcut Ctrl + K to add a hyperlink. At the left side of the window, click on ‘Place in this document’ and select the preferred slide in the list. Then click on ‘OK’.
5
Copy the transparent shape and repeat step 4. Do this for all menu buttons.
Want to know more? Go to the tab 'SLIDEBUILDER’ and click on the button ‘Inspiration'
Inspiration
Motivation
01
Approach
02
Algorithms
03
Results
04
Discussion
05
Conclusion
06
Notes: Introduce the structure of the presentation ?

## Slide 3: Motivation
Stroke is a prevalent cause of disability
Functional arm use in stroke rehabilitation
Home rehabilitation
Accessibility of wrist worn sensors vs leg-worn
Towards@HomeRehabilitation
Direct feedback during the day
End of the day analysis
sensors
Notes: Many of you are probably familiar with the towards@home application but to recap, it is

## Slide 4: Approach
Literature review of existing algorithms and datasets
Recording data
  Self recorded
  Stroke patients from Rijndam
Adapt existing algorithms
[1] QSense Motion. QSense Motion Capture Platform: User Manual. url: https://qsense-motion.com/downloads/User-Manual-QSense.pdf.

## Slide 5: Approach: Existing Algorithms
Looking for: IMUs on wrist
Wide Range of Gait Detection Algorithms available:
Signal Processing based
Machine Learning based
Multiple sensor locations
Shortlist most relevant:
  ElderNet, Straczkiewicz, Kheirkhanan, Hickey

## Slide 6: Approach: Existing Datasets
Looking for: IMUs on wrist, subjects performing ADL
Wide Range of Gait Datasets available:
Healthy subjects
Subjects with diagnosis of condition (PD)
Multiple sensor locations
Annotated
We shortlist most relevant:
  WISDM, WearGait, HMP, BioCliTe

## Slide 7: Approach: Recorded Data
Self recorded:
Normal walking
Edge cases (10)
  Using handrail, simulating stroke, using phone, using crutches or cane
Mixed tests
  Several alternating activities
  Including washing hands, reading a magazine, drawing, vacuuming
Clinical:
5 patients in total
  Patient 2 left out for analysis
Mixed test of alternating walking\non-walking activities
Activities adjusted for mobility level of the patient
  Included washing hands, making a puzzle, watering plants, using arm exercise machine
Free living: stroke patients, ADLs in the kitchen

## Slide 8: Algorithms
ML methods:
ElderNet
StrokeNet
Signal Processing:
Straczkiewicz
Hickey
Kheirkhahan

## Slide 9: Algorithms: ML Approaches - ElderNet
ElderNet:
  Existing deep-learning approach on acceleration data from wrist-worn sensors
  Optimised for elderly + impaired walk
  UK BioBank SSL Model Include RUSH MAP Fine-tune on Mobilise-D
  1D CNN: 5 layers
  Input: 10s windows
  Output: softmax probability of gait
  If prob > threshold GAIT
Fig: ElderNet development pipeline (credit: YonBrand)

## Slide 10: Algorithms: ML Approaches - StrokeNet
StrokeNet - Modification of ElderNet:
  Motivation: Specialise model to stroke gait
  Remove last (downsampling) layer shorter input windows
  Retrain on self-recorded data Stroke- and sensor-specific
  Obtain new weights for the classifier head
  2s windows with 1s stride
  If prob > threshold GAIT

## Slide 11: Algorithms: Signal Pro. - Straczkiewicz
"One-size fits most" signal processing based:
  Continuous Wavelet Transform: decompose Tri-axial accelerations
  Amplitude threshold, step frequency discriminator, temporal continuity of dominant frequency
Necessary adaptations:
  Simplified, real-time
  FFT on 2s window with 1s stride
  Amplitude, power and frequency thresholding
  Threshold Optimisation on self-recorded mixed data

## Slide 12: Algorithms: Signal Pro. - Hickey
Originally developed for lower back position
Threshold based
  Mean per window
  STD per window
Tuned to wrist worn position
Further tuned on the recorded data

## Slide 13: Algorithms: Signal Pro. - Kheirkhahan
Adaptive walking detection per 12s window
Originally for hip postion
  Adjusted to wrist position
Based on activity count
Uses overlapping window approach
Tuned of the self recorded data
  STD threshold check added in tuning

## Slide 14: Algorithms: Signal Pro. - Real-time approach
No knowledge of future data
2s buffer added at the beginning and the end
  13s total
Walking predictions are used to overwrite the previous windows predictions
Data from the two wrist can be fused

## Slide 15: Results
Cross dataset comparison
Clinical trials results
Wrist fusion
  StrokeNet
  Realtime implementation

## Slide 16: Cross Dataset comparison
F1 = performance metric for imbalanced datasets
Mixed results for all algos – likely due to subject differences + test setup (sampling freq)

## Slide 17: Results of Clinical Tests
Evaluation set: gives best indication of performance + generalisability
StrokeNet: best performing (outperforms Leg), good performance on patient with walker
Signal processing: good performance, unable to detect gait with walker

## Slide 18: Results of Clinical Tests – Walker
Walker present
Stable during walking
No walker present
Noisy during walking

## Slide 19: Fusion of wrists – StrokeNet
Strategies:
  Unaffected
  Affected
  Acceleration average
  Probability average
  Voting AND
  Voting OR
Best performing:
  Probability average
  F1 = 0.87 @ p = 0.5

## Slide 20: Fusion of wrists – Kheirkhahan
Improved performance for classification fusion
Outperforms single wrist classification
Without subject 1, F1 score of 0.81

## Slide 21: Discussion
Real-time vs End-of-day
Faulty and Insufficient data
StrokeNet improvements
Kheirkhahan improvements

## Slide 22: Real-time vs End-of-day
Real-time: runs onboard sensor to give real-time feedback to patient
  Computational size limit ~ 20 kB
  Processing time < window size
  Only use current and previous window data
End-of-day: Data of day uploaded for therapist to run energy analysis locally
  No limitations

## Slide 23: Faulty and Insufficient Data
Timestamps repeated
Discarded when preprocessing
  Discontinuities  less full windows
4 clinical trials evaluated
  1 walker, 1 unsupported, 2 with cane
Further tests necessary for complete analysis

## Slide 24: Limitations & Improvements
StrokeNet:
  With more data retrain again
  Perform hyperparameter optimisation
Kheirkhahan realtime:
  Inability to detect walking with a walker  evaluate the effect on the energy
  Difficulty with rhythmic motion  optimise for the needed frequencies

## Slide 25: Conclusion
End-of-day: StrokeNet (F1 = 0.87)
  Best fusion: Prob. Average
Real-time: Kheirkhahan (F1 = 0.81)
  Best fusion: AND
  Cannot detect gait with walker
Recommendations:
Further testing on the target demographic

## Slide 26: Afsluiter
Thank you for your attention

## Slide 27: Public Datasets – WISDM (20 Hz):
WISDM: 51 healthy participants, 18 activities for 3 minutes, smartphone and smartwatch

## Slide 28: Public Datasets – BioCliTe (50 Hz):
BioCliTe: 20 healthy subjects, 7 activities ~ 5 min, smartwatch

## Slide 29: Public Datasets – HMP (32 Hz):
HMP: 16 healthy volunteers, 14 Activities ~ sec-min, single wrist-worn accelerometer

## Slide 30: Public Datasets - WearGait:
WearGait: 33 PD + 19 age-matched controls, multiple sensors (wrist incl.), 6 activities ~ 3 min

## Slide 31: ROC curves